THE MORKOOL REFRIDGERATOR

# Text boxes

The MORKOOL REFRIDGERATOR will give every satisfaction. If properly installed. SO follow these instructions carefully.

It is recommended to install as shown in diagram marked A and B where outlet is shown entering kitchen chimney any

length of pipe can be used to carry outlet to chimney in either A or B. Keep in mind that the MORKOOL is entirely remote

from existing means and that heat in the outside of the Refrigerator, if anything, increases efficiency, so have no fear

In placing it next to the fuel stove as shown. In C the outlet is shown going out through the wall of building B. In C the vent pipe, which is 4 in downpipe for the house – hold model (No1) and 5in for the Station size (no2) should be as long as possible and be exposed to the sun, i.e. install Refrigerator on the sunny side of the building. Keep pipe well Clear of the roof and fit with revolving cowl to prevent back Draught. All joins to pipe to be soldered as they MUST BE AIRTIGHT. When going through brickwork, step around pipe With CEMENT TIGHTLY. The longer the pipe in C, the Greater the efficiency. Usually 12 feet.

CARE AND OPERATION – When the Refrigerator is installed as above, remove top lift out cooling unit of evaporation, and FILL trough with RAIN WATER to gauge. Saturate evaporator wall with water and replace with the high end of the evaporator to the FRONT of the cabinet. The Refrigerator is now in operation. All that is necessary to keep the Refrigerator in operation is to keep the trough full of water.

CARE of UNIT – This unit is constructed so as to give trouble free service, and is made in envelope type so as to facilitate easy removal for washing and boiling which should be done on its becoming soiled..

In the winter time, remove the fabric from frame, wash, press and store away. One of the outstanding features of the MORKOOL REFRIDGERATOR is that IT IS NEVER IDLE. FOODS can be kept in the MORKOOL all year round in a current of pure fresh air.

PLACE HOT FOODS, etc ON THE BOTTOM OF THE REFRIDGERATOR

INSTALLATION METHODS

Roof

Cowl

Grass

|||||||||||||||||||||||||||||

Picture Rail

Other room

Stove

Stove

A 		Floor 			        B 		                               Floor 			           C

In other room through to kitchen         In kitchen to Fireplace                                                       In any room to outside

Register

Kitchen